## Slide 1
How Lithium-Ion Battery Recycling Works
A First-Year Engineering Primer on Chemistry, Recovery, and Economics
Notes: Welcome. Today we will cover the fundamentals of lithium-ion battery recycling—the chemistry inside the cells, the three main recovery methods, and why making the economics work is the real engineering challenge.

## Slide 2
The Chemistry Inside a Spent Cell
What makes recycling both necessary and difficult
2
Notes: Before we talk about recycling, we need to understand what we are recovering. A lithium-ion battery contains valuable metals like cobalt, nickel, and lithium, but they are locked inside complex layered oxides and graphite anodes. The chemistry determines which recovery methods are viable.

## Slide 3
Key Components in a Li-Ion Cell
Cathode: lithium metal oxide (e.g., LiCoO₂, NMC)
Anode: graphite on copper foil
Electrolyte: lithium salt in organic solvents
Separator: porous polymer membrane
Casing: aluminum or steel
3
Notes: Each component must be separated or processed. The cathode contains the highest-value metals. The electrolyte is flammable and toxic, so it must be handled carefully. The casing and current collectors are often recycled as scrap metal.

## Slide 4
Three Main Recovery Methods
Pyrometallurgy, hydrometallurgy, and direct recycling
4
Notes: There are three established routes for recovering materials from spent batteries. Each has different trade-offs in energy use, material recovery rates, and capital cost. We will look at each in turn.

## Slide 5
Pyrometallurgy: Smelting It Out
Batteries are fed into a high-temperature furnace (over 1400°C)
Organic materials burn off; metals form an alloy
Cobalt and nickel recovered; lithium lost to slag
High energy use, low capital cost per ton
Works for mixed battery streams
5
Notes: Pyrometallurgy is the oldest method. It is robust and can handle mixed battery types, but it loses lithium to the slag. The energy cost is significant, and the process emits CO₂ from burning the electrolyte and separator.

## Slide 6
Hydrometallurgy: Leaching Metals in Solution
Batteries are shredded; black mass is leached with acid
Metals dissolved and selectively precipitated or extracted
High recovery rates for lithium, cobalt, nickel, manganese
Lower temperature, more chemical waste
Requires sorting by cathode chemistry
6
Notes: Hydrometallurgy achieves higher recovery rates, especially for lithium. But it requires the batteries to be sorted by chemistry, and the process generates acidic wastewater that must be treated. It is more capital-intensive than pyrometallurgy.

## Slide 7
Direct Recycling: Preserving the Cathode Structure
Cathode material is separated without breaking it down
Relithiation restores electrochemical capacity
Lowest energy use, highest material value retention
Still at pilot scale; sensitive to impurities
Best for single-chemistry streams
7
Notes: Direct recycling is the most elegant approach—it keeps the cathode structure intact and simply replenishes lithium. It uses the least energy and retains the most value. However, it is still in development and requires clean, sorted input streams.

## Slide 8
The Economic Reality
<5%
of spent Li-ion batteries are recycled today in many regions; collection and sorting costs often exceed recovered metal value
8
Notes: Despite the technical feasibility of all three methods, recycling rates remain low. The economics are the bottleneck: collection, transportation, sorting, and processing costs often exceed the value of recovered materials, especially when lithium and cobalt prices are low.

## Slide 9
Why Economics Are Hard
Collection and transport: batteries are hazardous goods
Sorting by chemistry adds labor or sensor cost
Metal prices fluctuate; recycling margins are thin
Low volume today means no economies of scale
Regulation varies widely by jurisdiction
9
Notes: the source material highlights that economics are the main challenge. Collection is expensive because batteries are classified as hazardous materials. Sorting requires either manual labor or X-ray fluorescence sensors. And the value of recovered metals depends on volatile commodity markets.

## Slide 10
Recycling Is a Systems Problem
Chemistry gives us the tools; engineering must make them economical at scale
10
Notes: To wrap up: lithium-ion battery recycling is technically feasible through pyrometallurgy, hydrometallurgy, or direct recycling. But the real challenge is designing collection systems, sorting processes, and business models that make recycling profitable. That is where you as engineers come in.